## Slide 1
SWS3009 · ADVANCE PROPOSAL
DeskMate
Team 11 — Loss Hunters
Wang Tianqi · Chen Zengchun · Gu Songtao · Lin Ziqi

## Slide 2
DESKMATE
GROUP 11 · LOSS HUNTERS
A MOVING DESKTOP COMPANION FOR FOCUS, WELL-BEING AND INTERACTION
ADVANCED PROJECT
DESKMATE
DESKTOP COMPANION
10 DAYS
Vision · deep learning · autonomous robotics
Wang Tianqi · Lin Ziqi
Gu Songtao · Chen Zengchun
Loss Hunters · Group 11
PRODUCT VISION
A desktop companion that sees context
and responds through motion and expression
TARGET USERS
Students and office workers
who stay at a desk for long periods
CORE PROBLEM
Important habits are easy to miss
when reminders are passive or easy to dismiss
DESIGN PRINCIPLE
Proactive, responsive
and fun enough to stay present on the desk
COURSE FIT
Deep-learning perception + autonomous robot control
Video + computer audio · moving parts · deep-learning automation · interactive feedback
01
Notes: The Advanced Model is optional and is introduced only when the Basic Model cannot classify continuous behaviour reliably. Candidate extensions include temporal posture classification, dynamic gesture recognition, phone-detector fine-tuning, multimodal off-task behaviour classification, noise-type recognition, and personalization. The recommended extension is a small TCN or GRU trained on normalized hand-landmark sequences with dimensions T by twenty-one by three. This input is compact, reduces background interference, and avoids training directly on raw video.

## Slide 3
PRODUCT OVERVIEW
HEALTH · FOCUS · COMPANIONSHIP
FROM PASSIVE REMINDERS TO A COMPANION THAT PERCEIVES AND ACTS
PRODUCT PROMISE
AWARE OF
DESK CONTEXT
PROACTIVE
Perceive → decide → move and respond
Reduce unnoticed long sitting
Interrupt harmful focus patterns
Make reminders visible and engaging
LONG SITTING
Detect prolonged seated or static states
then trigger a stretch or movement cue
SCREEN & EYE USE
Estimate face-to-screen distance
and sustained head / gaze direction
PHONE DISTRACTION
Detect persistent phone use
during an active focus session
PASSIVE SOFTWARE
Notifications are easy
to mute, ignore, or forget
DESKMATE RESPONSE
One event layer coordinates movement, display, servo and computer sound
The robot changes position or expression so the reminder becomes a physical interaction
02
Notes: The Advanced Model is optional and is introduced only when the Basic Model cannot classify continuous behaviour reliably. Candidate extensions include temporal posture classification, dynamic gesture recognition, phone-detector fine-tuning, multimodal off-task behaviour classification, noise-type recognition, and personalization. The recommended extension is a small TCN or GRU trained on normalized hand-landmark sequences with dimensions T by twenty-one by three. This input is compact, reduces background interference, and avoids training directly on raw video.

## Slide 4
CORE EXPERIENCE
PERCEIVE
Camera observes posture,
face, hands and phone
INTERPRET
Pre-trained models convert
frames into useful features
CONFIRM
Temporal logic checks that
the behaviour persists
RESPOND
Robot moves, turns, displays
and plays sound through the laptop
RESET
User gesture or cooldown
returns to monitoring
FOCUS SUPPORT
Start, pause and reset a focus timer
Detect persistent phone distraction
Celebrate completion with motion / display
WELL-BEING CUES
Track sitting and static duration
Estimate screen distance and head direction
Prompt short breaks and posture changes
COMPANION FEEDBACK
Face recognition can personalize greetings
Screen shows emoji, status and timer
Movement makes the response visible and playful
ONE LOOP, MULTIPLE MODALITIES
Video and laptop audio drive decisions; motion, display and sound close the interaction loop.
03
Notes: Frame-level predictions must be stabilized before they trigger a reminder. Moving averages, exponential smoothing, or majority voting reduce jitter, while duration and entry-exit thresholds prevent brief or oscillating states from generating events. Phone confidence, head direction, and system events can be fused, and gestures require confirmation across multiple frames. Low-confidence decisions return unknown, reminders use cooldown periods, and all thresholds remain adjustable through user testing.

## Slide 5
SYSTEM ARCHITECTURE
CAMERA / LAPTOP MIC
Video + computer audio
PI 5 OR LAPTOP
Perception and event logic
UNIFIED EVENTS
Confidence + duration gates
ARDUINO MEGA
Motor / servo control
ROBOT RESPONSE
Move, display, computer sound
PERCEPTION / DECISION
ROLE
Vision models
Pose, face, hand and phone
events
Temporal logic
Smooth, confirm and apply cooldown
gate
Runtime choice
Raspberry Pi 5 or laptop
deploy
Communication
USB serial JSON messages
serial
CONTROL / FEEDBACK
ROLE
Drive base
4 TT motors + HW-130 driver
motion
Interaction
64×48 display + two servos
feedback
Safety sensors
Ultrasonic + tracking modules
safety
Scope boundary
Two-wheel + caster and a mechanical arm remain optional mechanical extensions
04
Notes: The baseline validates the complete sensing-to-robot pipeline without training a task-specific model. Webcam frames and microphone signals are processed with OpenCV, timers, signal statistics, and hand-crafted thresholds, then converted into binary events. The supported functions include sitting duration, static posture, approximate screen distance, brightness, noise, simple gestures, and timer events. Phone classification, user identity, and complex dynamic gestures remain outside the baseline.

## Slide 6
DEEP LEARNING CORE
PRE-TRAINED MODELS · EDGE / PC
LAYER 01
PRE-TRAINED
PERCEPTION
POSE
MediaPipe Pose
Landmarker
FACE / EYE
MediaPipe Face
Landmarker
HAND
MediaPipe / cvzone
21 landmarks
PHONE
Object Detector +
EfficientDet-Lite0
IDENTITY*
Optional YuNet +
SFace embedding
LAYER 02
DERIVED
FEATURES
POSTURE
Body landmarks
Shoulder / neck / trunk angles
MOTION
Landmark displacement
Variance + static duration
EYE / HEAD
Eye landmarks + blendshape
Head pose + distance level
GESTURE
Five-finger state
Direction, speed, trajectory
DETECTION
Phone box + confidence
Identity similarity (optional)
LAYER 03
TEMPORAL +
RULE LOGIC
MOVING AVERAGE
Smooth frame-level features
MULTI-FRAME VOTING
Confirm stable state decisions
DURATION THRESHOLD
Emit only persistent states
REMINDER COOLDOWN
Avoid repeated interruptions
SUPPORT
PROGRAM LOGIC
Brightness statistics
Audio level / SPL
Clock and reminders
Robot actuation
05
Notes: The Basic Model is the main project deliverable and uses lightweight pre-trained models without custom training. MediaPipe provides pose, face, and hand landmarks; EfficientDet-Lite0 detects phones; and YuNet with SFace supports local user recognition. These models produce posture angles, motion variation, blink and head-pose features, gesture trajectories, detection confidence, and face similarity. Moving averages, multi-frame voting, duration thresholds, and reminder cooldowns stabilize the results on a standard CPU.

## Slide 7
UNIFIED EVENT OUTPUT
RAW MODEL OUTPUTS
KEYPOINTS
Body · face · hand
DETECTION
Class · box · confidence
IDENTITY
Embedding · similarity
GESTURE
Class · probability
AUDIO / STATE
Laptop noise level · state probability
STANDARDIZED EVENT
{
"event": "bad_posture",
"model_level": "basic",
"confidence": 0.91,
"duration_s": 38,
"evidence": {
"neck_angle_deg": 24.6
},
"suggested_action": "move_and_prompt"
}
EVENT VOCABULARY
bad_posture
static_too_long
screen_too_close
low_blink_rate
environment_too_bright
environment_too_dark
noise_too_high*
phone_usage_detected
off_task_behaviour
user_recognized
unknown_user
gesture_detected
DL MODULE
UNIFIED EVENT
CONTROLLER
06
Notes: The models produce landmarks, bounding boxes, confidence scores, face embeddings, gesture probabilities, noise measurements, and frame-level state probabilities. The deep learning module does not control the robot directly. Instead, it emits a standardized event containing the event name, model level, confidence, duration, supporting evidence, and a suggested action. The controller then maps that event to a robot expression, sound, or movement.

## Slide 8
HARDWARE & CONTROL
COMPUTE
1
Raspberry Pi 5 · high-level compute
2
Laptop · optional model runtime
3
IMX219 camera · video input
4
Arduino Mega 2560
motor + servo controller
5
USB serial link
6
Power bank for Raspberry Pi
separate 3S motor pack
7
Shared ground + protected wiring
MOTION
1
Four TT geared motors
2
HW-130 motor driver
3
Four-wheel differential drive
primary and safest base
4
Two-wheel + caster
exploratory configuration
Primary demo uses four-wheel differential drive
INTERACTION
1
64×48 monochrome display
2
MG90S + MG90 servos
3
Ultrasonic + tracking sensors
for obstacle and edge awareness
4
Speaker and microphone
through laptop if connected
Laptop audio supplies the second input modality
BUILD PRIORITY
SAFE BASE
4-wheel drive · camera · display
CORE AI
Pose · hand · phone · laptop audio
EXPLORE
2-wheel base · audio · arm if feasible
07
Notes: Video preprocessing converts OpenCV frames from BGR to RGB, samples the frame rate, crops relevant regions, normalizes model inputs, and preserves timestamps. Audio is converted to fixed-rate mono windows, with RMS or relative sound-pressure level used for volume detection and an optional Log-Mel spectrogram used for classification. Face samples are detected, aligned, normalized, and filtered for darkness, blur, or excessive angle. Baseline and Basic Model development require calibration and testing data, while Advanced Model training requires labeled landmark or multimodal sequences.

## Slide 9
AUTONOMOUS BEHAVIOUR
DETECT
Video frames and
current robot state
CONFIRM
Temporal voting and
confidence threshold
SELECT
Action priority with
distance and safety rules
ACT
Move, turn, servo, display
and sound through the laptop
COOLDOWN
Resume monitoring after
user response or timeout
SITTING TOO LONG
Show timer and stretch cue
Approach or turn toward the user
Return after acknowledgement
PHONE DISTRACTION
Display a refocus prompt
Move or react when usage persists
Gesture acknowledges the reminder
GESTURE INPUT
Start, pause or reset the focus timer
Robot confirms with display and motion
Manual stop remains available
AUTONOMOUS DOES NOT MEAN UNCONTROLLED
Low speed, distance limits, obstacle sensing and cooldowns remain active during every behaviour.
08
Notes: Frame-level predictions must be stabilized before they trigger a reminder. Moving averages, exponential smoothing, or majority voting reduce jitter, while duration and entry-exit thresholds prevent brief or oscillating states from generating events. Phone confidence, head direction, and system events can be fused, and gestures require confirmation across multiple frames. Low-confidence decisions return unknown, reminders use cooldown periods, and all thresholds remain adjustable through user testing.

## Slide 10
10-DAY DELIVERY PLAN
18–27 JULY 2026
BUILD CORE FIRST; ADD EXTENSIONS ONLY AFTER THE END-TO-END DEMO WORKS
DELIVERY STRATEGY
VERTICAL SLICE
THEN POLISH
MVP FIRST
Every stage ends with a runnable demo
Must: drive + video + laptop audio
Should: posture / phone / gesture DL
Could: identity, 2-wheel base, arm
DAYS 1–2 · FOUNDATION
Drive, sensors, power and serial link
Produce a remotely testable moving base
DAYS 3–4 · PERCEPTION
Camera + pose / face / hand / phone
Validate frame rate and event quality
DAYS 5–6 · RESPONSE
Unified events → Arduino actions
Add timer, display, servo and movement
DAYS 7–8 · INTEGRATE
Tune thresholds
and complete end-to-end scenarios
DAYS 9–10 · TEST + DEMO
Run scenario tests, polish behaviour, prepare slides and backup video
Failsafe: each AI event can be simulated so hardware and interaction remain demonstrable
09
Notes: The Advanced Model is optional and is introduced only when the Basic Model cannot classify continuous behaviour reliably. Candidate extensions include temporal posture classification, dynamic gesture recognition, phone-detector fine-tuning, multimodal off-task behaviour classification, noise-type recognition, and personalization. The recommended extension is a small TCN or GRU trained on normalized hand-landmark sequences with dimensions T by twenty-one by three. This input is compact, reduces background interference, and avoids training directly on raw video.

## Slide 11
APPENDIX: OPTIONAL EXTENSIONS
ONLY AFTER CORE DEMO
USE ONLY WHEN CONTINUOUS BEHAVIOUR IS NOT STABLE IN THE PRE-TRAINED PIPELINE
RECOMMENDED LEARNED EXTENSION
DYNAMIC GESTURE
TCN OR GRU
T × 21 × 3
normalized hand-landmark sequence
Wave, swipe, and circle classes
Low-dimensional training input
Lower background and privacy risk
CONTINUOUS POSTURE
Small MLP, 1D-TCN, or GRU
Normalized body-landmark sequence
PHONE DETECTOR
Fine-tune a lightweight detector
Small targets and partial occlusion
OFF-TASK BEHAVIOUR
TCN/GRU or multimodal MLP
Phone, head direction, idle time, events
AUDIO CLASSIFICATION
Pre-trained YAMNet via laptop
Requires an external microphone
PERSONALIZED CALIBRATION
User-specific distance, posture and usage baselines
Goal: reduce variation between users without making personalization a core dependency
10
Notes: The Advanced Model is optional and is introduced only when the Basic Model cannot classify continuous behaviour reliably. Candidate extensions include temporal posture classification, dynamic gesture recognition, phone-detector fine-tuning, multimodal off-task behaviour classification, noise-type recognition, and personalization. The recommended extension is a small TCN or GRU trained on normalized hand-landmark sequences with dimensions T by twenty-one by three. This input is compact, reduces background interference, and avoids training directly on raw video.